## Slide 1
🚀 TEAM FALCONS
TECHNICAL APPROACH
SMART INDIA HACKATHON 2026 | ISRO PS ID: 26169
🇮🇳 ISRO / DOS
❖ TECHNOLOGY STACK
🌐 Frontend & 3D Twin
Three.js (WebGL), HTML5 Canvas HUD, Chart.js, Vanilla CSS Glassmorphism, IBM Plex typography, 60 FPS WebSockets.
⚡ Backend Engine
Python 3.11+, FastAPI (ASGI), Uvicorn Server, Asyncio Event Loop, NumPy, SciPy (Vectorized Linear Algebra).
🧠 AI & Perception
YOLOv8-FSOC Beacon Detector, ONNX Runtime, TensorRT edge acceleration, Pinhole Camera Intrinsic Model.
🎯 Estimation & Control
6-DOF Extended Kalman Filter (EKF), Dual-Axis PID Controller with Anti-Windup & Slew Clamping (<= 45 deg/s).
🔬 Optical Physics & Link Budget
1550nm C-Band EDFA Model, Beer-Lambert Extinction, Gaussian Beam Profile, SNR and Complementary Error Function BER (Pe = 1/2 erfc(sqrt(SNR)/2sqrt(2))).
🔌 Hardware & Benchmarks
STM32 / ESP32 Micro-ROS, Serial CAN-Bus / gRPC, Pan-Tilt Brushless Gimbals, Pytest Suite, Automated 1-Click ISRO Benchmark Logger.
❖ FSOC AI Virtual Camera Tracking Engine Summary:
Custom YOLOv8 for sub-pixel beacon localization; 6-DOF EKF trajectory prediction during 2.0s cloud occlusions; dual-axis PID closed-loop actuation at 60 FPS (< 5ms latency) maintaining pointing error <= 8.72 mrad.
❖ CLOSED-LOOP SYSTEM ARCHITECTURE & DATA FLOW
[01] 3D Kinematics & Channel Engine
Target trajectory [X,Y,Z] in world frame, weather extinction, platform jitter
[02] Virtual Pinhole Camera Sensor
Projects 3D coordinates to 2D image plane (1920x1080) using intrinsic matrix K
[03] AI Beacon Detector (YOLOv8-FSOC)
Sub-pixel centroid & bounding box extraction (< 2.1 ms inference latency)
[04] 6-DOF Extended Kalman Filter (EKF)
State estimation [u, v, u_dot, v_dot, u_ddot, v_ddot] + 2.0s occlusion extrapolation
[05] Dual-Axis PID Gimbal Controller
Clamped slew (<= 45 deg/s) to maintain optical alignment within 8.72 mrad (0.50 deg)
[06] 1550nm FSOC Optical Physics & Link
Evaluates Beer-Lambert loss, RSSI (dBm), SNR (dB), and validates BER <= 1e-9
≤ 8.72 mrad
Coarse Threshold
60 FPS
Telemetry Rate
< 5.0 ms
Processing Latency
> 95.0%
Lock Retention

## Slide 2
🚀 TEAM FALCONS
TECHNICAL APPROACH & METHODOLOGY
SMART INDIA HACKATHON 2026 | ISRO PS ID: 26169
🇮🇳 ISRO / DOS
❖ 6-PHASE METHODOLOGY
1. Kinematics & Channel
3D target trajectory + wind turbulence & weather attenuation.
2. Camera Projection
Pinhole intrinsic projection matrix mapping [X,Y,Z] -> [u,v].
3. AI YOLOv8 Detection
Sub-pixel centroid localization with optical beacon filter.
4. 6-DOF EKF Estimation
Forward trajectory extrapolation across 2.0s cloud occlusions.
5. Dual-Axis PID Control
Clamped slew (<= 45 deg/s) to achieve pointing error <= 8.72 mrad.
6. Optical Link Validation
1550nm link budget: RSSI, SNR, and BER <= 1e-9 (10 Gbps Lock).
❖ SIMULATION TO HARDWARE MAPPING
Optical Perception:
• Sim: Synthetic pinhole projection • Hardware: 1550nm InGaAs SWIR Coarse Acquisition Camera
AI Target Detection:
• Sim: YOLOv8-FSOC ONNX model • Hardware: Jetson Orin / Embedded FPGA AI Accelerator
State Estimation:
• Sim: 6-DOF EKF Riccati filter • Hardware: Real-time C++ EKF flight controller firmware
Gimbal Pointing:
• Sim: Dual-axis PID with slew limit • Hardware: Direct CAN-bus PWM to Pan-Tilt Direct Motors
Optical Physics:
• Sim: Gaussian beam & Beer-Lambert • Hardware: 100mW EDFA Laser Diode + APD Photodiode
Mission Telemetry:
• Sim: 60 FPS WebSocket data bus • Hardware: ISTRAC Ground Station CCSDS / ZeroMQ Protocol
❖ TECHNOLOGIES USED
🎨 FrontEnd
React / Three.js (WebGL), HTML5 Canvas Telescope HUD, Chart.js, Vanilla CSS Glassmorphism.
⚡ BackEnd
Python 3.11+, FastAPI (ASGI), Uvicorn, NumPy, SciPy (Vectorized Math), WebSockets.
🧠 AI & Estimation
YOLOv8-FSOC, 6-DOF Extended Kalman Filter (EKF), Dual-Axis PID Slew Controller.
📊 Benchmarking
Automated 1-Click ISRO Performance Logger (JSON Summary, CSV Dataset, PDF Report).
📡 Optical Physics
1550nm FSOC Laser Link Budget, Beer-Lambert Extinction, Gaussian Beam Loss, SNR & BER.

## Slide 3
🚀 TEAM FALCONS
ALGORITHMIC RIGOR & MATHEMATICAL FORMULATION
MATHEMATICAL RIGOR & CONTROL EQUATIONS | ISRO PS ID: 26169
🇮🇳 ISRO / DOS
1. Pinhole Camera Projection Model
• 3D to 2D Homogeneous Coordinate Transform: [u, v, 1]^T = (1/Z_c) * K * [R | T] * [X_w, Y_w, Z_w, 1]^T • Intrinsic Matrix K = diag(f_x, f_y, 1) + [0, 0, c_x; 0, 0, c_y; 0, 0, 0] • Optical Sensor Noise: eta ~ N(0, sigma_pixel^2) with sigma = 0.5 px • Real-time sub-pixel centroid extraction at 1920x1080 resolution.
2. 6-DOF Extended Kalman Filter (EKF)
• State Vector: x = [u, v, u_dot, v_dot, u_ddot, v_ddot]^T • State Transition: x_{k|k-1} = F * x_{k-1} + w_k, w_k ~ N(0, Q) • Measurement Update: z_k = H * x_k + v_k, v_k ~ N(0, R) • Kalman Gain: K_k = P_{k|k-1} H^T (H P_{k|k-1} H^T + R)^{-1} • 2.0s Occlusion Extrapolation: P_k updates via continuous Riccati propagation.
3. Dual-Axis PID Gimbal Slew Dynamics
• Pixel Error to Angular Rate: e_theta = (u - c_x)/f_x, e_phi = (v - c_y)/f_y • Control Law: u(t) = K_p e(t) + K_i int_0^t e(tau) dtau + K_d (de/dt) • Dynamic Anti-Windup: Clamps integral accumulator during high slews • Slew Rate Limiter: |omega_az| <= 45 deg/s, |omega_el| <= 45 deg/s • Pointing Error Target: theta_pointing <= 8.72 mrad (0.50 deg).
4. 1550nm FSOC Optical Physics & Link Budget
• Received Power: P_RX(dBm) = P_TX + G_TX + G_RX - FSPL - L_pointing - A_atm • Gaussian Pointing Loss: L_pointing = -8.686 * (theta_pointing / theta_div)^2 dB • Beer-Lambert Extinction: A_atm(R) = 10 * gamma_ext * R * log10(e) • Bit Error Rate (BER): P_e = 0.5 * erfc(sqrt(SNR) / (2 * sqrt(2))) • Carrier Lock: BER <= 1e-9 & SNR >= 25 dB enables 10 Gbps data throughput.